## Slide 1: CircuitSeer: RTL Post-PnR Delay Prediction via Coupling Functional and Structural Representation
Sanjay Gandham1, Joe Walston2, Sourav Samanta2, Linxiang Yin1, Hao Zheng1, Mingjie Lin1, Stelios Diamantidis​2
1 University of Central Florida 2 Synopsys

## Slide 2: Outline
Background and Motivation​
Traditional Flow for Delay Evaluation and Shortcomings​
Prior Work and Limitations
CircuitSeer​
Evaluation​

## Slide 3: Background and Motivation​
With the end of Dennard scaling and decline of Moore’s law, performance improvement comes at a cost.

## Slide 4: Background and Motivation​
With the end of Dennard scaling and decline of Moore’s law, performance improvement comes at a cost.
Power, Performance, Area (PPA) is becoming increasingly important during the hardware design process.

## Slide 5: Background and Motivation​
However, traditional RTL design is primarily functionality-oriented
With the end of Dennard scaling and decline of Moore’s law, performance improvement comes at a cost.
Power, Performance, Area (PPA) is becoming increasingly important during the hardware design process.

## Slide 6: Background and Motivation​
However, traditional RTL design is primarily functionality-oriented
With the end of Dennard scaling and decline of Moore’s law, performance improvement comes at a cost.
Power, Performance, Area (PPA) is becoming increasingly important during the hardware design process.
How can we enable PPA-oriented RTL Design?

## Slide 7: Traditional Flow for Delay Evaluation
Digital Designer
Spec

## Slide 8: Traditional Flow for Delay Evaluation
Digital Designer
Spec
RTL

## Slide 9: Traditional Flow for Delay Evaluation
Digital Designer
Spec
RTL
Elaboration
Boolean Minimization
Technology Mapping
Technology Dependent Optimization
Logic Synthesis
Netlist

## Slide 10: Traditional Flow for Delay Evaluation
Digital Designer
Spec
RTL
Elaboration
Boolean Minimization
Technology Mapping
Technology Dependent Optimization
Logic Synthesis
Netlist
Post-
Synthesis
Delay

## Slide 11: Traditional Flow for Delay Evaluation
Digital Designer
Spec
RTL
Elaboration
Boolean Minimization
Technology Mapping
Technology Dependent Optimization
Logic Synthesis
Netlist
Post-
Synthesis
Delay
Missing wirelength information leading to inaccurate delay estimates

## Slide 12: Traditional Flow for Delay Evaluation
Digital Designer
Spec
RTL
Elaboration
Boolean Minimization
Technology Mapping
Technology Dependent Optimization
Logic Synthesis
Netlist
Post-
Synthesis
Delay

## Slide 13: Traditional Flow for Delay Evaluation
Digital Designer
Spec
RTL
Elaboration
Boolean Minimization
Technology Mapping
Technology Dependent Optimization
Logic Synthesis
Netlist
Post-
Synthesis
Delay
Partitioning
Floor Planning
Placement
Routing
Layout
Physical Design

## Slide 14: Traditional Flow for Delay Evaluation
Digital Designer
Spec
RTL
Elaboration
Boolean Minimization
Technology Mapping
Technology Dependent Optimization
Logic Synthesis
Netlist
Post-
Synthesis
Delay
Partitioning
Floor Planning
Placement
Routing
Layout
Physical Design
Post-
Place and Route
Delay

## Slide 15: Traditional Flow for Delay Evaluation
Digital Designer
Spec
RTL
Elaboration
Boolean Minimization
Technology Mapping
Technology Dependent Optimization
Logic Synthesis
Netlist
Post-
Synthesis
Delay
Partitioning
Floor Planning
Placement
Routing
Layout
Physical Design
Post-
Place and Route
Delay
Long Logic Synthesis and Physical Design runtime

## Slide 16: Traditional Flow for Delay Evaluation
Digital Designer
Spec
RTL
Elaboration
Boolean Minimization
Technology Mapping
Technology Dependent Optimization
Logic Synthesis
Netlist
Post-
Synthesis
Delay
Partitioning
Floor Planning
Placement
Routing
Layout
Physical Design
Post-
Place and Route
Delay
Accurate delay estimates are inaccessible early in the RTL design process

## Slide 17: Prior Work: AI/ML-Based Delay Predictor
RTL
Logic Synthesis
Netlist
Layout
Physical Design
Functionality Preserving Transformations
Netlist Structure Dependent Operations

## Slide 18: Prior Work: AI/ML-Based Delay Predictor
RTL
Logic Synthesis
Netlist
Layout
Physical Design
Functionality Preserving Transformations
Netlist Structure Dependent Operations
Post-Synthesis Delay
From RTL
[1, 2, 3]
[1] Ceyu Xu et al. Sns’s not a synthesizer: a deep- learning-based synthesis predictor. In Proc. of ISCA, 2022.
[2] Prianka Sengupta et al. How good is your verilog rtl code? a quick answer from machine learning. In Proc. of ICCAD, 2022.
[3] Wenji Fang et al. Masterrtl: A pre-synthesis ppa estimation framework for any rtl design. In Proc of ICCAD, 2023.

## Slide 19: Prior Work: AI/ML-Based Delay Predictor
RTL
Logic Synthesis
Netlist
Layout
Physical Design
Functionality Preserving Transformations
Netlist Structure Dependent Operations
Post-Synthesis Delay
From RTL
[1, 2, 3]
[1] Ceyu Xu et al. Sns’s not a synthesizer: a deep- learning-based synthesis predictor. In Proc. of ISCA, 2022.
[2] Prianka Sengupta et al. How good is your verilog rtl code? a quick answer from machine learning. In Proc. of ICCAD, 2022.
[3] Wenji Fang et al. Masterrtl: A pre-synthesis ppa estimation framework for any rtl design. In Proc. of ICCAD, 2023.
Transformer and Machine Learning Models for Functional Representation Learning

## Slide 20: Prior Work: AI/ML-Based Delay Predictor
RTL
Logic Synthesis
Netlist
Layout
Physical Design
Functionality Preserving Transformations
Netlist Structure Dependent Operations
Post-PnR Delay
From Netlist
Post-Synthesis Delay
From RTL
[1, 2, 3]
[4]
[4] Ahmed Agiza et al. Graphsym: Graph physical synthesis model. In Proc. of ICCAD, 2023.

## Slide 21: Prior Work: AI/ML-Based Delay Predictor
RTL
Logic Synthesis
Netlist
Layout
Physical Design
Functionality Preserving Transformations
Netlist Structure Dependent Operations
Post-PnR Delay
From Netlist
Post-Synthesis Delay
From RTL
[1, 2, 3]
[4]
[4] Ahmed Agiza et al. Graphsym: Graph physical synthesis model. In Proc. of ICCAD, 2023.
Graph Neural Network Model
For Structural Representation Learning

## Slide 22: Prior Work: AI/ML-Based Delay Predictor
RTL
Netlist
Layout
Physical Design
Functionality Preserving Transformations
Netlist Structure Dependent Operations
Post-PnR Delay
From Netlist
Post-Synthesis Delay
From RTL
[1, 2, 3]
[4]
Post-PnR Delay
From RTL
(This Work)
Logic Synthesis

## Slide 23: Prior Work: AI/ML-Based Delay Predictor
RTL
Netlist
Layout
Physical Design
Functionality Preserving Transformations
Netlist Structure Dependent Operations
Post-PnR Delay
From Netlist
Post-Synthesis Delay
From RTL
[1, 2, 3]
[4]
Post-PnR Delay
From RTL
(This Work)
Logic Synthesis
Couple Functional and Structural Representation Learning

## Slide 24: Challenges with Post-PnR Delay Prediction
RTL
Netlist
Layout
Physical Design
Functionality Preserving Transformations
Netlist Structure Dependent Operations
Logic Synthesis

## Slide 25: Challenges with Post-PnR Delay Prediction
RTL
Netlist
Layout
Physical Design
Functionality Preserving Transformations
Netlist Structure Dependent Operations
Logic Synthesis
Logic Synthesis significantly modifies the circuit structure.

## Slide 26: Challenges with Post-PnR Delay Prediction
RTL
Netlist
Layout
Physical Design
Functionality Preserving Transformations
Netlist Structure Dependent Operations
Logic Synthesis
Logic Synthesis significantly modifies the circuit structure.
The initial circuit representation is structurally dissimilar to the netlist

## Slide 27: Challenges with Post-PnR Delay Prediction
RTL
Netlist
Layout
Physical Design
Functionality Preserving Transformations
Netlist Structure Dependent Operations
Logic Synthesis
Logic Synthesis significantly modifies the circuit structure.
Extract Synthesis-invariant topological Information from RTL for structural learning
The initial circuit representation is structurally dissimilar to the netlist

## Slide 28: CircuitSeer: Prediction Flow

## Slide 29: CircuitSeer: Prediction Flow
Generate Initial Circuit Representation (Unoptimized Netlist)

## Slide 30: CircuitSeer: Prediction Flow
Generate Initial Circuit Representation (Unoptimized Netlist)
Graph Transformation to extract synthesis-invariant topological information

## Slide 31: CircuitSeer: Prediction Flow
Generate Initial Circuit Representation (Unoptimized Netlist)
Functional learning from logic cells of a path
Graph Transformation to extract synthesis-invariant topological information

## Slide 32: CircuitSeer: Prediction Flow
Generate Initial Circuit Representation (Unoptimized Netlist)
Functional learning from logic cells of a path
Structural learning using the transformed graph
Graph Transformation to extract synthesis-invariant topological information

## Slide 33: CircuitSeer: Prediction Flow
Generate Initial Circuit Representation (Unoptimized Netlist)
Functional learning from logic cells of a path
Structural learning using the transformed graph
Delay Prediction using learned circuit representation
Graph Transformation to extract synthesis-invariant topological information

## Slide 34: CircuitSeer: Unoptimized Netlist
Table: Number of combinational and sequential cells of unoptimized netlist (u) and post-synthesis Netlist (ps)
represents the percentage difference in u and ps

## Slide 35: CircuitSeer: Unoptimized Netlist
Table: Number of combinational and sequential cells of unoptimized netlist (u) and post-synthesis Netlist (ps)
represents the percentage difference in u and ps
of combinational cells is high indicating large dissimilarity between the netlists.

## Slide 36: CircuitSeer: Unoptimized Netlist
Table: Number of combinational and sequential cells of unoptimized netlist (u) and post-synthesis Netlist (ps)
represents the percentage difference in u and ps
of sequential cells remain minimal indicating high similarity.
of combinational cells is high indicating large dissimilarity between the netlists.

## Slide 37: CircuitSeer: Graph Transformation

## Slide 38: CircuitSeer: Graph Transformation
Unoptimized Netlist and Post Synthesis Netlist are structurally dissimilar.

## Slide 39: CircuitSeer: Graph Transformation
Unoptimized Netlist and Post Synthesis Netlist are structurally dissimilar.
Traversing logic cones to identify the path relations between timing endpoints.

## Slide 40: CircuitSeer: Graph Transformation
Unoptimized Netlist and Post Synthesis Netlist are structurally dissimilar.
Traversing logic cones to identify the path relations between timing endpoints.
Generate graph based on the identified paths.

## Slide 41: CircuitSeer: Graph Transformation
Figure: Adjacency matrices of transformed unoptimized netlist and transformed post-synthesis Netlist

## Slide 42: CircuitSeer: Inference Flow
From Graph Traversal

## Slide 43: CircuitSeer: Inference Flow
From Graph Traversal

## Slide 44: CircuitSeer: Inference Flow
From Graph Traversal

## Slide 45: CircuitSeer: Inference Flow
From Graph Traversal
From Graph Generation
GNN Model

## Slide 46: CircuitSeer: Inference Flow
From Graph Traversal
From Graph Generation
GNN Model
Edge Regression

## Slide 47: Evaluation: Implementation and Baselines
CircuitSeer Implementation
Implemented in Python using Pytorch Geometric and the Hugging face library
ASIC Implementation
Employed Synopsys Fusion Compiler using the compile_fusion flow to perform ASIC implementation
Constrained hardware to near-maximum operational frequency.
Implemented using SAED32 nm tech library
Baselines
Transformer [1]
XGBoost [2]
[1] Ceyu Xu et al. Sns’s not a synthesizer: a deep- learning-based synthesis predictor. In Proc. of ISCA, 2022.
[2] Prianka Sengupta et al. How good is your verilog rtl code? a quick answer from machine learning. In Proc. of ICCAD, 2022.

## Slide 48: Evaluation: Hardware Designs
Collected from ITC’99[1], IWLS’05[2], OpenCores[3] and RISC-V cores.
14 Training designs with 364k paths.
4 Testing designs with 39k paths.

## Slide 49: Evaluation: Metrics
MAPE: Mean Average Error Percentage
MAPE K: MAPE for longest K% paths
R: Correlation coefficient
R2: Determination coefficient

## Slide 50: Evaluation: MAPE

## Slide 51: Evaluation: MAPE
CircuitSeer shows an average 𝑅2 correlation of 0.625, compared to 0.1875 and 0.1275 achieved by Transformer and XGBoost
CircuitSeers shows a lower average MAPE 50 of 17.5% compared to 27.3% and 27.5% of baselines.

## Slide 52: Evaluation: Scatter Plot

## Slide 53: Evaluation: Scatter Plot
Histogram showing higher peaks closer to the diagonal

## Slide 54: Evaluation: Heatmap
Metrics

## Slide 55: Evaluation: Heatmap
Metrics
CircuitSeer shows tighter clustering, especially at the critical paths

## Slide 56: Evaluation: Runtime Evaluation
Figure: Average path delay Inference runtime comparison
Figure: Breakdown of CircuitSeer inference time

## Slide 57: Evaluation: Runtime Evaluation
CircuitSeer inference model is at a per-path granularity leading to significant speedup
CircuitSeer shows an average speedup of 713 times compared to Fusion Compiler Synthesis run
Figure: Average path delay Inference runtime comparison
Figure: Breakdown of CircuitSeer inference time

## Slide 58: Evaluation: Ablation Study
Figure: R score comparison
Table: MAPE for top 25% longest paths

## Slide 59: Evaluation: Ablation Study
Comparing CircuitSeer (CS) with CircuitSeer without GNN (CS w/o GNN)
Average R score improves by 0.45
Average MAPE 25 reduces by 8.8%
Figure: R score comparison
Table: MAPE for top 25% longest paths

## Slide 60: Conclusion
In this work, we
We present CircuitSeer, the first pre-synthesis delay prediction framework to accurately estimate the post-PnR metrics.
We propose graph transformations to extract synthesis-invariant structural information from the initial circuit representation
Introduced structural and functional characteristics to the model
Achieved lower error and higher correlation compared to SOTA models

## Slide 61: Thank You Questions?
Contact Information
Sanjay Gandham: sanjay.gandham@ucf.edu